## Slide 1: DevNet Learning Forum
3 – Network APIs

## Slide 2: Agenda
Review
What’s API?
Yang and Netconf
REST API and Restconf
Demo: ACI, DNA API

## Slide 3: Review

## Slide 4: Network APIs

## Slide 5
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
What is an API?

## Slide 6
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Application Programming Interface (API)
”It’s a way for two pieces of software to talk to each other”

## Slide 7: For a long time.. Humans were the only users

## Slide 8: For a long time.. Humans were the only users
User asks for data or takes action by interacting with UI
Software displays results in User Interface (UI)

## Slide 9: But what about when the user is another software system….
Software asks for data or takes action by interacting with API
Software returns
results via API
My Software System
Your Software System

## Slide 10
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
The API is the User Interface for software systems

## Slide 11
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
APIs are sets of requirements that govern how one application can talk to another.

## Slide 12: An API is like an electrical outlet.
What would it be like to power an hair dryer without an outlet?
Open wall
Strip wires
Splice wires together
Understand all the wires
in the wall
The outlet is a service that conforms to specifications.
Sockets deliver 120 volts of alternating current (AC) operating at 60Hz
Sets expectation on behalf of consuming devices and provider.

## Slide 13: An API is like …
An API (Application Programming Interface) is best thought of as a contract
provided by one piece of computer software to another.

## Slide 14: APIs help developers create apps that benefit the end user.
Yelp asks for Map
Data
Google Maps returns map data via API
Users sees list of restaurants close to them

## Slide 15
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
APIs are often referred to as “an
engine of innovation.”
-- Programmable Web

## Slide 16: Command Line Interface (CLI)
Designed for Humans… so more
a UI than API
but...
Network Management Systems
Expect Scripts
Paramiko/Netmiko
NAPALM
#!/usr/bin/expect -f
send "conf t\n" expect "(config)#"
send ”hostname my_switch\n" expect "(config)#"
send "ntp server 10.10.10.101\n"
expect "(config)#"
send "ip domain-name domain.intra\n" expect "(config)#"
send "end\n"
expect "#"
send "write mem\n"
expect "#"

## Slide 17: Simple Network Management Protocol (SNMP)
“designed as a programmatic interface between management applications and devices”*
Widely used for monitoring
Limited use for configuration
Network Management Systems
primary consumer
* https://tools.ietf.org/html/rfc3535

## Slide 18: Simple Object Access Protocol (SOAP)
Mature standard designed by
Microsoft
Used to build “Web Services” (software available over the internet)
Typically uses HTTP, and dependent on XML
Sometimes considered complex
and rigid

## Slide 19: Representational State Transfer (REST)
API framework intended to build simpler web services than SOAP
Another use for the HTTP
protocol
Popular due to performance, scale, simplicity, and reliability
Technically an API framework
* More detailed coverage in later lessons

## Slide 20: XML-RPC and JSON-RPC
Simple frameworks for
communicating over HTTP
RPC = Remote Procedure Call
  When one system requests
another system to execute code
Offer XML and JSON data formats respectively
HTTP POST REQUEST BODY: [
{
"jsonrpc": "2.0",
"method": "cli", "params":
{
"cmd": "show version", "version": 1
},
"id": 1
}
]

## Slide 21: NETCONF (NETwork CONFiguration) Protocol
Designed as replacement for
SNMP
Standardized in 2006 / Updated
2011
Leverages SSH and XML
Defines transport and
communication
  Titled coupled to YANG for data
* More detailed coverage in later lessons

## Slide 22: RESTCONF Protocol
Provide REST API like interface
to network
Standardized in 2017
Supports XML and JSON
Defines transport and
communication
  Titled coupled to YANG for data
* More detailed coverage in later lessons

## Slide 23
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Yang and Netconf

## Slide 24: The Network is No Longer Isolated

## Slide 25: What about SNMP?
SNMP works “reasonably well for device monitoring”
RFC 3535: Overview of the 2002 IAB Network Management Workshop – 2003 https://tools.ietf.org/html/rfc3535
Typical config: SNMPv2 read-only
community strings
Typical usage: interface statistics queries and traps
Empirical Observation: SNMP is not
used for configuration
  Lack of Writeable MIBs
  Security Concerns
  Difficult to Replay/Rollback
  Special Applications

## Slide 26: Model Driven Programmability
NETCONF – 2006 – RFC 4741
(RFC 6241 in 2011)
YANG – 2010 – RFC 6020
RESTCONF – 2017 – RFC 8040
gRPC – 2015 – OpenSource
project by Google

## Slide 27: Transport (Protocol) vs Data (Model)
NETCONF
RESTCONF
gRPC
YANG

## Slide 28: Three Meanings of “YANG”

## Slide 29: YANG Modeling Language
module ietf-interfaces { import ietf-yang-types {
prefix yang;
}
container interfaces {
list interface { key "name"; leaf name {
type string;
}
leaf enabled { type boolean; default "true";
}
}
Example edited for simplicity and brevity
Module that is a self-contained top- level hierarchy of nodes
Uses containers to group related nodes
Lists to identify nodes that are stored in sequence
Each individual attribute of a node is represented by a leaf
Every leaf must have an
associated type

## Slide 30: What is a Data Model?
A data model is simply a well understood and agreed upon method to describe "something". As an example, consider this simple "data model" for a person.
Person
  Gender - male, female, other
  Height - Feet/Inches or Meters
  Weight - Pounds or Kilos
  Hair Color - Brown, Blond, Black,
Red, other
  Eye Color - Brown, Blue, Green,
Hazel, other

## Slide 31: What might a YANG Data Model describe?

## Slide 32: Where do Models Come From?
Standard definition
(IETF, ITU, OpenConfig, etc.)
Compliant with standard
ietf-diffserv-policy.yang
ietf-diffserv-classifer.yang
ietf-diffserv-target.yang
Industry
Standard
Vendor
Specific
Vendor definition
(i.e. Cisco)
Unique to Vendor Platforms cisco-memory-stats.yang cisco-flow-monitor
cisco-qos-action-qlimit-cfg
https://github.com/YangModels/yang

## Slide 33: Where to get the Models?
https://github.com/YangModels/yang
“YANG modules from standard organizations such as the IETF, open source such as Open Daylight or vendor specific modules”

## Slide 34: YANG Data Models
The model can be displayed and represented in any number of
formats depending on needs at the time. Some options include:
YANG Language
Clear Text
XML
JSON
HTML/JavaScript

## Slide 35: Working with YANG Models
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
DevNet$ pyang –f tree ietf-interfaces.yang
module: ietf-interfaces
+--rw interfaces
| +--rw interface* [name]
¦ | +--rw | name | string
¦ | +--rw | description? | string
¦ | +--rw | type | identityref
¦ | +--rw | enabled? | boolean
¦ | +--rw | link-up-down-trap-enable? | enumeration {if-mib}?
Example output edited for simplicity and brevity
netprog_basics/network_device_apis/yang/ietf-interfaces.yang

## Slide 36: Using pyang
© 2017 Cisco and/or its affiliates. All rights reserved.
Cisco Confidential
Python YANG Library
Validate and display
YANG files
Many formats for display
  Text: tree
  HTML: jstree
module: ietf-interfaces
+--rw interfaces
face* [n
+--rw name
stri
string
| +--rw inter
|
|
|
|
|
identityref boolean
enumeration {if-mib}?
+--ro interfaces-state
+--ro interface* [name]
+--ro name
+--ro type
+--ro admin-status
+--ro oper-status
+--ro last-change?
int32 {if-mib}? yang:phys-address interface-state-ref interface-state-ref yang:gauge64
+--ro if-index
+--ro phys-address?
+--ro higher-layer-if*
+--ro lower-layer-if*
+--ro speed?
+--ro statistics
yang:date-and-time
yang:counter64
+--ro discontinuity-time
+--ro in-octets?
[OUTPUT REMOVED]
Module Name
Example edited for simplicity and brevity
nLg eaf
string identityref
enumeration {if-mib}?
enumeration yang:dateD-aandta-tTimyepe
container list
container
list
Kaemey]
+--rw description?
+--rw type
+--rw enaObplteiodn?al
+--rw link-up-down-trap-enable?
Read Only

## Slide 37
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Demo Time!
github yang repo
yang files
pyang

## Slide 38
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Network Device Data in YANG

## Slide 39: Actual Device Data Modeled in YANG
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 40: Use NETCONF to Retrieve ietf-interfaces data
NETCONF details covered in
another session
ncclient provides a Python
client for NETCONF
Using built-in library to print reply
  xml.dom.minidom
netprog_basics/network_device_apis/yang/device_info.py
netprog_basics/network_device_apis/yang/example1.py

## Slide 41: Use NETCONF to Retrieve ietf-interfaces data
<interfaces xmlns="urn:ietf:params:xml:ns:yang:ietf-interfaces">
<interface>
<name>GigabitEthernet1</name>
<description>DON'T TOUCH ME</description>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip">
<address>
<ip>10.10.10.48</ip>
<netmask>255.255.255.0</netmask>
</address>
</ipv4>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
</interface>
<interface>
<name>GigabitEthernet2</name>
<type xmlns:ianaift="urn:ietf:params:xml:ns:yang:iana-if-type">ianaift:ethernetCsmacd</type>
<enabled>true</enabled>
<ipv4 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
<ipv6 xmlns="urn:ietf:params:xml:ns:yang:ietf-ip"/>
</interface>
</interfaces>
interfaces container
interface node
Leaf
netprog_basics/network_device_apis/yang/device_info.py
netprog_basics/network_device_apis/yang/example1.py
Namespace = Capability = Model
DevNet$ python example1.py

## Slide 42: Introducing the NETCONF Protocol
Some key details:
Initial standard in 2006
with RFC4741
Latest standard
is RFC6241 in 2011
Does NOT explicitly define
content

## Slide 43: NETCONF Protocol Stack

## Slide 44: Transport - SSH
$ ssh admin@192.168.0.1 -p 830 -s netconf
admin@192.168.0.1's password:
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-monitoring</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-interfaces</capability>
[output omitted and edited for clarity]
</capabilities>
<session-id>19150</session-id></hello>]]>]]>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.0</capability>
</capabilities>
</hello>]]>]]>
SSH Login
Server (Agent)
sends hello
Client (Manager)
sends hello
Example edited for simplicity and brevity

## Slide 45
Transport - SSH
$ ssh admin@192.168.0.1 -p 830 -s netconf
admin@192.168.0.1's password:
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-netconf-monitoring</capability>
<capability>urn:ietf:params:xml:ns:yang:ietf-interfaces</capability>
[output omitted and edited for clarity]
</capabilities>
<session-id>19150</session-id></hello>]]>]]>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.0</capability>
</capabilities>
</hello>]]>]]> Example edited for simplicity and brevity
Don’t NETCONF Like this!

## Slide 46: Understanding the Capabilities List
Two General Types
Base NETCONF capabilities
Data Models Supported
DevNet$ python example1.py
Here are the NETCONF Capabilities
urn:ietf:params:netconf:base:1.0 urn:ietf:params:netconf:base:1.1
.
urn:ietf:params:xml:ns:yang:ietf-interfaces?module=ietf-interfaces&revision=2014-05-08&features=pre-
provisioning,if-mib,arbitrary-names&deviations=ietf-ip-devs
.
http://cisco.com/ns/ietf-ip/devs?module=ietf-ip-devs&revision=2016-08-10
.
http://cisco.com/ns/yang/Cisco-IOS-XE-native?module=Cisco-IOS-XE-native&revision=2017-02-07
Example edited for simplicity and brevity

## Slide 47: Understanding the Capabilities List
urn:ietf:params:xml:ns:yang:ietf-interfaces
? module=ietf-interfaces
& revision=2014-05-08
& features=pre-provisioning,if-mib,arbitrary-names
& deviations=ietf-ip-devs
.
http://cisco.com/ns/ietf-ip/devs
? module=ietf-ip-devs & revision=2016-08-10
Data Model Details
Model URI
Module Name and Revision Date
Protocol Features
Deviations – Another model that modifies this one
Example edited for simplicity and brevity

## Slide 48: Messages - Remote Procedure Call (RPC)

## Slide 49: Operations - NETCONF Actions
Operation | Description
<get> | Retrieve running configuration and device state information
<get-config> | Retrieve all or part of specified configuration data store
<edit-config> | Loads all or part of a configuration to the specified configuration data store
<copy-config> | Replace an entire configuration data store with another
<delete-config> | Delete a configuration data store
<commit> | Copy candidate data store to running data store
<lock> / <unlock> | Lock or unlock the entire configuration data store system
<close-session> | Graceful termination of NETCONF session
<kill-session> | Forced termination of NETCONF session

## Slide 50: NETCONF Data Stores
Data Store Key Points
Entire or partial configuration
"running" is the only mandatory data store
Not all data stores are writeable
A "URL" data store is supported by IOS to
enable <config-copy>
Every NETCONF message must target a
data store
result = m.get_config('running')

## Slide 51: NETCONF Communications

## Slide 52: Yang Explorer
https://github.com/CiscoDevNet/yang-explorer

## Slide 53: NETCONF and Python: ncclient
Full NETCONF Manager
implementation in Python
  https://ncclient.readthedocs.io
Simplifies connection and
communication.
Deals in raw XML
From: http://ncclient.readthedocs.io/en/latest/

## Slide 54
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Demo Time!
netconf explorer
ncclient_interface_config.py

## Slide 55
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
RESTAPI and Restconf

## Slide 56: Just Another Use for the HTTP Protocol
Representational state transfer
(REST)
API framework built on HTTP
APIs often referred to as web services
Popular due to performance,
scale, simplicity, and reliability

## Slide 57: Requests and Response, the REST API Flow

## Slide 58: Requests and Response, the REST API Flow

## Slide 59: Requests and Response, the REST API Flow

## Slide 60: The URI: What are you Requesting?
The location of the data or object
of interest on the server
Parameters
  Details to scope, filter, or clarify a
request. Often optional.
http://maps.googleapis.com/maps/api/geocode/json?address=sanjose
Server or Host
http:// or https://
  Define whether secure or open
http
Server or Host
  Resolves to the IP and port to
connect to
Resource Parameters
Resource

## Slide 61: HTTP Methods: What to do?
HTTP Verb | Typical Purpose (CRUD) | Description
POST | Create | Used to create a new object, or resource. Example: Add new book to library
GET | Read | Retrieve resource details from the system. Example: Get list of books from the library
PUT | Update | Typically used to replace or update a resource. Can be used to modify or create. Example: Update the borrower details for a book
PATCH | Update | Used to modify some details about a resource. Example: Change the author of a book
DELETE | Delete | Remove a resource from the system. Example: Delete a book from the library.

## Slide 62: Response Status Codes: Did it work?
Status Code | Status Message | Meaning
200 | OK | All looks good
404 | Not Found | Resource not found

## Slide 63: Response Status Codes: Did it work?
Status Code | Status Message | Meaning
200 | OK | All looks good
201 | Created | New resource created
400 | Bad Request | Request was invalid
401 | Unauthorized | Authentication missing or incorrect
403 | Forbidden | Request was understood, but not allowed
404 | Not Found | Resource not found
500 | Internal Server Error | Something wrong with the server
503 | Service Unavailable | Server is unable to complete request

## Slide 64: Headers: Details and meta-data
Header | Example Value | Purpose
Content-Type | application/json | Specify the format of the data in the body
Accept | application/json | Specify the requested format for returned data
Authorization | Basic dmFncmFudDp2YWdyYW50 | Provide credentials to authorize a request
Date | Tue, 25 Jul 2017 19:26:00 GMT | Date and time of the message
Used to pass information between client and server
Included in both REQUEST and RESPONSE
Some APIs will use custom headers for authentication or other purpose

## Slide 65: Data: Sending and Receiving
Contained in the body
POST, PUT, PATCH requests
typically include data
GET responses will include data
Format typically JSON or XML
  Check “Content-Type” header
{
'title': 'Hamlet', 'author': 'Shakespeare'
}

## Slide 66: HTTP Authentication and Security
None: the Web API resource is public, anybody can place call.
Basic HTTP: a username and password are passed to the server in an
encoded string.
  Authorization: Basic ENCODEDSTRING
Token: a secret generally retrieved from the Web API developer portal.
Keyword (ie token) is API dependent
  Authorization: Token aikasf8adf9asd9akasdf0asd
OAuth: Standard framework for a flow to retrieve an access token from an
Identity Provider.
  Authorization: Bearer 8a9af9adadf0asdf0adfa0af
Authorization can be short-lived and require refreshing of tokens

## Slide 67: Many Options for Working with REST APIs
curl
  Linux command line application
Postman
  Chrome browser plugin and application
Requests
  Python library for scripting
Swagger
  Dynamic API Documentation
Browser Developer Tools
  View traffic and details within browser

## Slide 68: The Internet Chuck Norris Database
© 2017 Cisco and/or its affiliates. All rights reserved.
Cisco Confidential
DevNet$ curl https://api.icndb.com/jokes/random
{
"type": "success", "value": {
"id": 201,
"joke": "Chuck Norris was what Willis was talkin' about.", "categories": []
}
}
DevNet$ curl https://api.icndb.com/jokes/random?limitTo=nerdy
{
"type": "success",
"value": {
"id": 537,
"joke": "Each | hair | in | Chuck | Norris's | beard | contributes | to make | the world's largest DDOS.",
"categories": | [ |  |  |  |  |  |  | 
"nerdy"
]
}
}
http://www.icndb.com/api/
No authentication needed
Well constructed API with many options

## Slide 69
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Demo Time!
curl
postman
requests

## Slide 70: RESTCONF Details
https://tools.ietf.org/html/rfc8040
“an HTTP-based protocol that provides a programmatic interface for accessing data defined in YANG…”
RFC 8040 - January 2017
Uses HTTPS for transport
Tightly coupled to the YANG
Provides JSON or XML
data model definitions
data
formats

## Slide 71: What about NETCONF?

## Slide 72: RESTCONF Protocol Stack & Transport

## Slide 73: Operations - HTTP CRUD
RESTCONF | NETCONF
GET | <get> , <get-config>
POST | <edit-config> (operation="create")
PUT | <edit-config> (operation="create/replace")
PATCH | <edit-config> (operation="merge")
DELETE | <edit-config> (operation="delete")

## Slide 74: Content - XML or JSON
HTTP Headers
Content-Type: Specify the type of data being sent from the client
Accept: Specify the type of data being requested by the client
RESTCONF MIME Types
application/yang-data+json
application/yang-data+xml

## Slide 75: Constructing RESTCONF URIs
https://<ADDRESS>/<ROOT>/data/<[YANG MODULE:]CONTAINER>/<LEAF>[?<OPTIONS>]
ADDRESS - Of the RESTCONF Agent
ROOT - The main entry point for RESTCONF requests.
Discoverable at https://<ADDRESS>/.well-known/host-meta
data - The RESTCONF API resource type for data
  The “operations” resource type used to access RPC operations available
[YANG MODULE:]CONTAINER - The base model container being
used. Providing the module name is optional.
LEAF - An individual element from within the container
[?<OPTIONS>] - optional parameters that impact returned results.

## Slide 76: URL Creation Review
https://<ADDRESS>/restconf/data/ietf-interfaces:interfaces/interface=GigabitEthernet1?depth=unbounded
module: ietf-interfaces
+--rw interfaces
| +--rw interface* [name]
| +--rw name
| +--rw description?
| +--rw type
| +--rw enabled?
| +--rw link-up-down-trap-enable?
string string identityref boolean
enumeration {if-mib}?
Options Examples:
depth=unbounded
Follow nested models to end. Integer also supported
content=[all, config, nonconfig]
Query option controls type of data returned.
fields=expr
Limit what leafs are returned
Key:
https://<ADDRESS>/<ROOT>/data>/<[YANG MODULE:]CONTAINER>/<LEAF>[?<OPTIONS>]
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 77: Postman: Powerful but Simple REST API Client
Quickly test APIs in GUI
Save APIs into Collections for
reuse
Manage multiple environments
Auto generate code from API
calls
Standalone Application or
Chrome Plugin
https://www.getpostman.com

## Slide 78: Setup Environment for RESTCONF
Add variables for host, and
credentials
Reference anywhere with
{{variable name}} syntax

## Slide 79: Get Capabilities List via RESTCONF
GET
/restconf/data/netconf-state/capabilities
Add RESTCONF Headers
  Content-Type and Accept application/yang-data+json (or xml)
Configure Basic Auth with username
and password variables

## Slide 80
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Demo Time!
postman
python requests

## Slide 81: Summary
Data Model
Transport Protocol

## Slide 82: Hands-on
Use Python with Netconf (ncclient) to modify Interface-Config
Use Python with Restconf (requests) to modify Interface-Config

## Slide 83: Continue to study..
Learn network programmability basics (DevNet Video Courses)
  https://developer.cisco.com/video/net-prog-basics/
Python Tutorial
  https://www.learnpython.org/