## Slide 1: DevNet Learning Forum
4 – Application Hosting

## Slide 2: Agenda
Review
App-hosting
Guestshell
IOx

## Slide 3: Review

## Slide 4: App-hosting

## Slide 5: Current Application Challenges
Not enough network bandwidth
Most of the data is not interesting
The use of data may be at the edge
Computation can be optimized for some purposes Data normalization
Data redirection based on the content of the data
Data time stamping, algorithmic ownership
Data Reduction
Filtering
Latency Optimization
Partitioning
Application Simplification Dynamic Changes Analytic Support

## Slide 6: Empowering the Edge – Leverage the Network!
Existing hardware
footprint
No need for separate compute machinery
Integrated security
Reduced latency
& bandwidth cost
Billing
Analytic
Systems
IoT Applications
Business Applications
Management

## Slide 7: Cloud, Fog, Edge Computing

## Slide 8: Applications in Fog Computing
What is Fog Computing?
  An application architecture design combining compute, storage, control, management, and inter-communication of edge devices and clients
  Extension of the cloud down to the things
  One of the pillars of the Cisco IoT System
Why do we need another concept?
  Fog refers to a unique problem domain
  Fog addresses network issues of latency, bandwidth and operational issues of autonomous operation, in-flow data analysis, and management overload
Fog Computing
INTERNET OF THINGS
Fog Computing
Management and Automation
Network Connectivity
Security Cyber and Physical
Data Analytics
Application Enablement Platform
APPLICATIONS

## Slide 9: Fog Computing Architecture
Data Center
and Cloud
Core
Edge
Embedded
and Sensors
Controllers, Management Systems, Billing, Operations, etc.
IoT PaaS Platforms
Business
Applications
Analytics
Applications
Application
Application
Application

## Slide 10: Who wants to run apps in the network?
Infrastructure Engineers
Configuration and operations
management
Python scripts
Linux Utilities
Application Developers
Distributed Applications
IOT Applications
VMs and/or Containers

## Slide 11: Network Application Hosting Spectrum
Script Hosting
Python
Access platform
details
Integrate with events
Utility Hosting
Linux utilities
RPMs
Containers
Application Code + Dependencies
LXC and Docker
support
Small VM
Complete control
Limited resource
needs
Linux KVM
Full Compute
Significant resource needs
Bare-metal or
Hypervisor

## Slide 12: Cisco Application Hosting Technologies
Script Hosting
Utility Hosting
• Python • Linux utilities
• Access platform • RPMs
details
• Integrate with events
Containers
Small VM
• Application Code + Complete control
Dependencies • Limited resource
• LXC and Docker needs
support • Linux KVM
Full Compute
• Significant resource needs
• Bare-metal or
Hypervisor
Guest Shell
Cisco IOx
UCS
Express

## Slide 13: What is the Guest Shell?
64-bit Linux environment running on IOS XE and NX-OS platforms
Install, update, and operate 3rd party Linux apps (e.g. Puppet, Chef, Splunk)
Bundled with Python
Intended for agent or script
hosting
Network OS
Linux applications
Guest Shell
Open Application Container
API

## Slide 14
Host applications and services at the network edge across different hardware platforms
A compute platform, application framework, and software development kit
Manage life cycle aspects of
applications
What is Cisco IOx?
Cisco IOx
Application
+
Linux
+
Cisco IOS

## Slide 15: What is Cisco UCS Express
Cisco UCS Blade server installed and running in router/switch
Bare-metal or hypervisor
operating systems supported
Independent server
management (from network)

## Slide 16: Guestshell

## Slide 17: Cisco Application Hosting Technologies
Script Hosting
Utility Hosting
• Python • Linux utilities
• Access platform • RPMs
details
• Integrate with events
Containers
Small VM
• Application Code + Complete control
Dependencies • Limited resource
• LXC and Docker needs
support • Linux KVM
Full Compute
• Significant resource needs
• Bare-metal or
Hypervisor
Guest Shell
Cisco IOx
UCS
Express

## Slide 18: What is the Guest Shell?
64-bit Linux environment running on IOS XE and NX-OS platforms
Install, update, and operate 3rd party Linux apps (e.g. Puppet, Chef, Splunk)
Bundled with Python
Intended for agent or script
hosting
Network OS
Linux applications
Guest Shell
Open Application Container
API

## Slide 19: General Guest Shell Preparation
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
IOS XE Steps
Enable IOX on the device
Configure guest shell network
connectivity
Enable Guest Shell
Configure environment DNS and proxy requirements within Guest Shell
NX-OS Steps
Guest Shell is enabled by
default on NX-OS
Configure environment DNS and proxy requirements within Guest Shell

## Slide 20: Application Hosting: Networking
Routing
Container
Container
VM
Bridging
L2 interface
L3 interface
VirtualPortGroup X
SVI
10.0.0.2
10.0.0.3
10.0.0.6
10.0.0.1/24
Ge0/0/1
Ge0/0/2
Ge0/0/3
Ge0/0/11
Ge0/0/12
Ge0/0/13
12.0.0.3/24
IOS XE
12.0.0.1/24
12.0.0.2/24
10.0.0.5
Svc Bridge1
eth0
eth0
eth0
eth1
13.0.0.1
10.0.0.10
eth0
Container
Mgmt Bridge0
eth0
Management VRF
Ge0/0
eth1
172.19.0.23
172.19.0.24
AppGigEthernet X
Notes: VPG = Virtual Port Group

## Slide 21: IOS XE Step 1: Enabling IOx
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
IOx Manages the application
hosting on IOS XE
Guest Shell is just one use of
IOx
Notes
  IOx service take 3 minutes to start
  IOx service (HA) may not run
iosxe1#conf t iosxe1(config)#iox iosxe1(config)#exit
iosxe1#sh iox-service
Machine types supported
Machine types disabled
: LXC
: KVM
IOx Infrastructure Summary:
---------------------------
IOx service (CAF) : Running IOx service (HA) : Not Running IOx service (IOxman) : Running Libvirtd : Running
iosxe1#
Output edited for clarity

## Slide 22: IOS XE Step 2: Create Virtual Port Group
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Valid on routing platforms
only
Used to provide network connectivity to Guest Shell container
Commands to be entered shown
conf t
interface VirtualPortGroup 0
ip add 192.168.35.1 255.255.255.0
no shut
exit

## Slide 23: IOS XE Step 3: Create NAT Entry
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Valid on routing platforms only
Used to NAT traffic from Guest Shell off box
  Example: to access Internet resources
  Note: Inbound access to Guest Shell
requires additional NAT
Alternative to NAT is route to
VirtualPortGroup address space
Commands to be entered shown
* Command entered on single line in router
conf t
interface VirtualPortGroup0
ip nat inside
! Interface connected to local network
interface GigabitEthernet1
ip nat outside
ip access-list standard NAT_ACL
permit 192.168.0.0 0.0.255.255
ip nat inside source list NAT_ACL \*
interface GigabitEthernet1 overload

## Slide 24: IOS XE Step 4: Enable Guest Shell
VPG and IP only needed on
routing platforms
Guest Shell Life-cycle
  guestshell disable
    Removes access and kills the
current session
    Files and data are preserved
  guestshell destroy
    Deletes the guest shell file system
    All data is lost
! Entered from Enable Mode (not config)
! All entered on single line
guestshell enable VirtualPortGroup 0
guest-ip 192.168.35.2
name-server 208.67.222.222
show app-hosting list
App id State
------------------------------------------
guestshell RUNNING
Commands to be entered shown
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 25: Accessing and Using Guest Shell
Linux commands can be run
directly from the IOS CLI
Log into guest shell by running
guestshell run bash
The Linux environment can be customized by editing .bashrc or .bash_profile
iosxe1#guestshell run pwd
/home/guestshell
iosxe1#guestshell run bash
[guestshell@guestshell ~]$ ls -l
total 0
[guestshell@guestshell ~]$ ping 8.8.8.8
PING 8.8.8.8 (8.8.8.8) 56(84) bytes of data.
64 bytes from 8.8.8.8: icmp_seq=2 ttl=62 time=70.5 ms
64 bytes from 8.8.8.8: icmp_seq=3 ttl=62 time=70.1 ms
^C
--- 8.8.8.8 ping statistics ---
3 packets transmitted, 2 received, 33% packet loss,
time 2008ms
rtt min/avg/max/mdev = 70.108/70.345/70.583/0.356 ms [guestshell@guestshell ~]$
Commands to be entered shown
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 26: Environment Setup: DNS Servers and Proxies
DNS resolution within Guest Shell independent of host platform
IOS XE configures name-server within guestshell enable
NX-OS must explicitly configure
within /etc/resolv.conf
Any required proxies must be configured on both IOS XE and NX-OS
[guestshell@guestshell ~]$ cat /etc/resolv.conf nameserver 208.67.222.222
[guestshell@guestshell ~]$ ping pool.ntp.org -c 1 PING pool.ntp.org (128.138.141.172) 56(84) bytes of data.
64 bytes from utcnist2.colorado.edu (128.138.141.172): icmp_seq=1 ttl=62 time=91.3 ms
Commands to be entered shown
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 27: Accessing the CLI from the Guest Shell
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
dohost command built into Guest Shell
Send commands directly to the router
Limited to exec privilege commands. No access to config mode.
[guestshell@guestshell ~]$ dohost 'show ip int bri'
Interface | IP-Address | OK? | Method | Status | Protocol
GigabitEthernet1 | 10.0.2.15 | YES | DHCP | up | up
GigabitEthernet2 | unassigned | YES | unset | administratively | down down
GigabitEthernet3 | unassigned | YES | unset | administratively | down down
VirtualPortGroup0 | 192.168.35.1 | YES | manual | up | up
[guestshell@guestshell ~]$ dohost 'show log | inc DHCP'
*Jul 27 18:51:09.796: %DHCP-6-ADDRESS_ASSIGN: Interface GigabitEthernet1 assigned DHCP address 10.0.2.15, mask 255.255.255.0, hostname iosxe1

## Slide 28: Installing Applications within Guest Shell
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
YUM
  Package manager for Linux systems.
  Install, update and remove applications
  ’repos’ or file repositories
[guestshell@guestshell ~]$ sudo yum install git
Loaded plugins: fastestmirror
=====================================================================================================================
Package Arch Version Repository Size
=====================================================================================================================
Installing:
git x86_64 1.8.3.1-6.el7_2.1 base 4.4 M
Installed:
git.x86_64 0:1.8.3.1-6.el7_2.1
Complete!
[guestshell@guestshell ~]$ git –version git version 1.8.3.1
Git
Installed via yum
Access code from GitHub and other repositories
Useful for distribution of custom
applications.
Output edited for brevity and clarity

## Slide 29: Using Python for Network Programming
Scripts executed locally on switch
or router
Ideal for
  Provisioning (ie ZTP)
  Automating event responses (ie EEM)
  Application Development
  IOT
Scripts executed externally from
switch or router
Use API to interact with network
Ideal for
  Configuration management automation
  Telemetry/operational data
  Controller use cases
”On-Box” Python ”Off-Box” Python
Python
Device OS
 | Python |  | 
 |  | API | 
Device OS |  |  | 
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 30: On-Box Python Features in IOS XE and NX-OS
Interactive Python prompt
Run Python scripts directly on box
Includes a Cisco Python API library
for interacting with host device
Integration with Day Zero Deployment (ZTP and POAP)
Call Python Scripts with Embedded
Event Manager (EEM)
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 31: Interactive Python Prompt
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
At enable prompt guestshell run python
Interactive prompt inside a secured Guest Shell environment on the
device
Run Python commands right on box
iosxe1#guestshell run python
Python 2.7.5 (default, Jun 17 2014, 18:11:42)
[GCC 4.8.2 20140120 (Red Hat 4.8.2-16)] on linux2
Type "help", "copyright", "credits" or "license" for more information.
>>> x = "hello world"
>>> print(x)
hello world
>>>
Output edited for brevity and clarity

## Slide 32: Python Script
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
At enable prompt
guestshell run python /flash/script_name.py [args]
#guestshell run ls /flash/netprog_basics/application_hosting/python_onbox
hello_world.py
! Single line command
# guestshell run python
/flash/netprog_basics/application_hosting/python_onbox/hello_world.py
Hello World!
Output edited for brevity and clarity

## Slide 33: Installing Python Libraries
Use pip just like any other Python Environment*
sudo pip install <module>
iosxe1#guestshell run bash
[guestshell@guestshell ~]$ sudo pip install requests
Collecting requests
.
.
Installing collected packages: chardet, certifi, urllib3, idna, requests
Successfully installed certifi-2017.7.27.1 chardet-3.0.4 idna-2.6 requests-
2.18.4 urllib3-1.22
[guestshell@guestshell ~]$
Output edited for brevity and clarity
* Some libraries may not install due to memory or compiler issues depending on Guest Shell version and platform
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 34: Cisco Python CLI API
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Permits Python calls to use CLI commands directly and return results
Integrated into Python
interpreter inside Guest Shell
Enabled by adding library cli
  import cli
Command | Description
cli.cli(cmd) | Runs cli command(s) and returns result. Example: cli(“sh ver ; sh int”)
cli.clid(cmd)* | Runs cli command(s) and returns JSON output. Example: clid(“sh ver ; sh int”)
cli.clip(cmd) | Runs cli command(s) and prints result Example: clip(“sh ver ; sh int”)
cli.configure(cmd)** | Run a list of configuration commands. Example: cli.configure([“int lo1”, ”no shut”])
cli.configurep(cmd) ** | Run a list of configuration commands and print result. Example: cli.configure([“int lo1”, ”no shut”])
* - NX-OS Only
** - IOS XE Only

## Slide 35: Cisco Python API
Output edited for brevity and clarity
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
iosxe1#guestshell run python >>> import cli >>> cli.cli("show ip int brief") '\nInterface IP-Address OK? Method Status Protocol\nGigabitEthernet1 10.10.20.21 YES NVRAM up up \nGigabitEthernet2 unassigned YES NVRAM administratively ..' >>> cli.clip("show ip int brief") |  |  |  |  | 
Interface | IP-Address | OK? | Method | Status | Protocol
GigabitEthernet1 | 10.10.20.21 | YES | NVRAM | up | up
GigabitEthernet2 | unassigned | YES | NVRAM | administratively | down down
GigabitEthernet3 | unassigned | YES | NVRAM | administratively | down down
VirtualPortGroup0 | 192.168.35.1 | YES | NVRAM | up | up

## Slide 36: Cisco Python API
>>> cli.configurep(["int loop100", "desc Python Loop", "ip add 192.168.0.1
255.255.255.0"])
Line 1 SUCCESS: int loop100 Line 2 SUCCESS: desc Python Loop
Line 3 SUCCESS: ip add 192.168.0.1 255.255.255.0
>>> cli.clip("sh run int loop100") Building configuration...
Current configuration : 92 bytes
!
interface Loopback100
description Python Loop
ip address 192.168.0.1 255.255.255.0
end
Output edited for brevity and clarity
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 37: Day Zero Provisioning
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
(IOS XE/XR = ZTP / NX-OS POAP)
Automates process of upgrading
images and installing configurations
Utilizes DHCP for new device to find information
  Option 150 – provides location of TFTP
server that contains the Python script
  Option 67 – Python script file path on
TFTP server
Returned script might have basic copy information to install both image and configuration file
Python
Script
Network Device
1
2
3
4
TFTP
DHCP
Script
Guest Shell
5
Config
Startup Config?

## Slide 38: Embedded Event Manager
Configure the event manager applet to run a Python script in response
to the event
iosxe1(config)#event manager applet interface_Lo100_Shutdown
iosxe1(config-applet)#event syslog pattern "Interface Loopback100, changed
state to administratively down"
iosxe1(config-applet)#action 0.0 cli command "en"
iosxe1(config-applet)#action 1.0 cli command "guestshell run python
/flash/netprog_basics/application_hosting/python_onbox/eem_intf_up.py lo100"
iosxe1(config-applet)#exit
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Output edited for brevity and clarity

## Slide 39: Embedded Event Manager
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Manually trigger the event
iosxe1#term mon
iosxe1#debug event manager action cli
iosxe1#conf t iosxe1(config)#int lo100 iosxe1(config-if)#shut
Output edited for brevity and clarity

## Slide 40: Embedded Event Manager
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
*Oct
*Oct
2 20:44:57.843: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback100, changed state to down
2 20:44:57.843: %LINK-5-CHANGED: Interface Loopback100, changed state to administratively down
2 20:44:57.850: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : CTL : cli_open called.
2 20:44:57.850: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT : iosxe1>
2 20:44:57.851: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : IN : iosxe1>en
2 20:44:57.861: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT : iosxe1#
*Oct
*Oct
*Oct
*Oct
*Oct
2 20:44:57.861: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : IN : iosxe1#guestshell run
python /flash/netprog_basics/application_hosting/python_onbox/eem_intf_up.py lo100
*Oct
2 20:44:59.576: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT : Line 1 SUCCESS:
interface lo100
*Oct
*Oct
*Oct
*Oct
*Oct
*Oct
*Oct
2 20:44:59.576: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT : Line 2 SUCCESS: no shut
2 20:44:59.576: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT :
2 20:44:59.576: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT :
2 20:44:59.577: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : OUT : iosxe1#
2 20:44:59.577: %HA_EM-6-LOG: interface_Lo100_Shutdown : DEBUG(cli_lib) : : CTL : cli_close called.
2 20:44:59.577:
2 20:44:59.577: tty is now going through its death sequence
*Oct
*Oct
2 20:45:01.541: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback100, changed state to up
2 20:45:01.542: %LINK-3-UPDOWN: Interface Loopback100, changed state to up
Output edited for brevity and clarity
Verify with debug logs

## Slide 41
Demo Time!
guestshell
hello_world.py

## Slide 42: IOx

## Slide 43: Cisco Application Hosting Technologies
Script Hosting
Utility Hosting
• Python • Linux utilities
• Access platform • RPMs
details
• Integrate with events
Containers
Small VM
• Application Code + Complete control
Dependencies • Limited resource
• LXC and Docker needs
support • Linux KVM
Full Compute
• Significant resource needs
• Bare-metal or
Hypervisor
Guest Shell
Cisco IOx
UCS
Express

## Slide 44
Enables hosting applications at the network edge across different hardware platforms
A compute platform, application framework, and software development kit
Manage life cycle aspects of
applications
What is Cisco IOx?
Cisco IOx
Application
+
Linux
+
Cisco IOS
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 45: Why Cisco IOx?
Distributed Compute
  Run, manage and monitor
applications within the Fog
Secure Communications
  Use IOS networking and security
services
Powerful Integration
  Connect sensors to the cloud with IoT integration and middleware services
IOx
Compute
Application Management
IOS
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Routing/Switching Network Security Access Control

## Slide 46: IOx Applications
Packages of code and
resources deployed to IOx
Choice of language
Packaging Types
  Containerized
    Linux Container (LXC)
    Docker Tooling
  Virtual Machine (KVM)
  Platform as a Service
(Python and Java)
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential

## Slide 47: IOx Supported Platforms
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
https://developer.cisco.com/docs/iox/#!platform-support-matrix/platform-support-matrix

## Slide 48: Cisco IOx Core Components
© 2017 Cisco and/or its affiliates. All rights reserved. Cisco Confidential
Cisco Application Hosting Framework (CAF)
  The application framework that runs at the edge on the device
IOx SDK
  A software development kit that helps packaging an application to make it IOx-ready
ioxclient
  A command-line utility to help developers to interact with CAF, packaging
IOx Local Manager
  A web management interface resident with the CAF to manage a local device
Fog Director
  Management software running in the network that manages application lifecycle at scale

## Slide 49: Cisco IOx Application Development Overview
Performed on the IOx platform
Performed on the Workstation
Start
Code
Compile / Link
Test / Debug
Package
Install
Configure
Upload
Test / Debug
Release

## Slide 50: IOx Applications
Types of Applications
Docker
  Support for using the Docker toolchain to deploy IOx applications has been added to
IOx 1.2
Kernel Virtual Machine (KVM)
  A VM application is a virtual machine that contains the full OS (kernel and root filesystem) along with the application code and dependencies in a single package.
Linux Container (LXC)
  A Container application is a single package of the root file system, application code and dependencies like libraries and native binaries.

## Slide 51: Native Docker Support
Catalyst 9000
Catalyst 9300 – 16.12.1 Catalyst 9400 - 17.1.1 Catalyst 9500 * Catalyst 9600 *
Note: Catalyst 9200 do not support Application Hosting
* Roadmap

## Slide 52: Application Development - Docker
Native Docker App
C9K supports native Docker container starting from IOS XE 16.12 release.
An open platform for developing, shipping, and running applications.
Allow to package an application with all of its dependencies into a standardized unit for software development.

## Slide 53: Why Docker ?
Virtual Machine Includes application, binaries & libraries, an entire guest OS.
Docker Container format for Linux containers that makes the process of creating and maintaining containers easier.
Server
Docker Engine
Bins/Libs
Bins/Libs
App A
App B
}
MBs
Host OS
Server
Host OS
Hypervisor
Guest OS
Guest OS
Bins/Libs
Bins/Libs
App A
App B
}
GBs

## Slide 54: Docker Architecture
Notes: Docker client
It is the primary user interface to Docker. It accepts commands from the user and communicates back and forth with a Docker daemon.
Docker daemon
It runs on a host machine. The user does not directly interact with the daemon, but instead through the Docker client with the RESTful api or sockets.

## Slide 55: Docker Benefits
Fast (deployment, migration, restarts)
Secure
Lightweight (save disk & CPU)
Open Source
Simplify DevOps
Version control capabilities
Notes: Flexible: Even the most complex applications can be containerized.
Lightweight: Containers leverage and share the host kernel.
Interchangeable: You can deploy updates and upgrades on-the-fly.
Portable: You can build locally, deploy to the cloud, and run anywhere.
Scalable: You can increase and automatically distribute container replicas.
Stackable: You can stack services vertically and on-the-fly.

## Slide 56: Docker Workflow – Docker Hub
Pull Docker Image
1
Deploy App
2
docker save myapp > myapp.tar
docker pull <app>
DockerTM

## Slide 57: Docker Workflow -Custom App
Dockerfile
1
docker build -t <app> .
Build Docker Image
2
Deploy App
3
App Descriptor (Optional)
docker save myapp > myapp.tar
DockerTM
Application File
FROM ubuntu:18.04 as base RUN apt-get update -yq && apt-get install -yq python COPY poll-temperature.py /usr/bin/poll-temperature.py RUN chmod 777 /usr/bin/poll-temperature.py CMD /usr/bin/poll-temperature.py
#!/usr/bin/Python
import time import os
os.makedirs("/var/volatile/log") f = open('/var/log/poll-temp.log', 'w’)
while (1): s = "%s %s polling temperature ...\n" % (time.strftime("%d/%m/%Y"), time.strftime("%I:%M:%S")) f.write(s) f.flush() time.sleep(5)

## Slide 58: Validated Apps- DevNet Eco System Exchange
Cisco will not provide any support to third-party apps and open source apps unless specifically called out.
Such apps, however, will be validated for compatibility on Cisco® Catalyst® 9000 switches.
DevNet ecosystem will indicate the partners who have worked on Cisco Catalyst 9000 switches.
ISC DHCP Server
tshark
iPerf

## Slide 59
Application Management
CLI
REST
REST
Custom App
Docker
Custom App
Docker
Host OS (IOS XE Kernel)
Cisco Application Framework
Cisco DNA-C
CLI
Cisco DNA Center
3rd Party App
Docker
3rd Party App
Docker
3rd
Party App
Docker
CLI
REST
Fog
Director

## Slide 60: Application Hosting: Networking
Routing
Container
Container
VM
Bridging
L2 interface
L3 interface
VirtualPortGroup X
SVI
C9K
10.0.0.2
10.0.0.3
10.0.0.6
10.0.0.1/24
Ge0/0/1
Ge0/0/2
Ge0/0/3
Ge0/0/11
Ge0/0/12
Ge0/0/13
12.0.0.3/24
IOS XE
12.0.0.1/24
12.0.0.2/24
10.0.0.5
Svc Bridge1
eth0
eth0
eth0
eth1
13.0.0.1
10.0.0.10
eth0
Container
Mgmt Bridge0
eth0
Management VRF
Ge0/0
eth1
172.19.0.23
172.19.0.24
AppGigEthernet X
Notes: VPG = Virtual Port Group

## Slide 61: App Management: IOS XE CLI
Enable and Verify
cat9k# conf t
cat9k(config)# iox
cat9k(config)# ip http server
cat9k# sh iox-service
...
IOx Infrastructure Summary:
---------------------------
IOx service (CAF) : Running
IOx service (HA) : Running
IOx service (IOxman) : Running
Libvirtd : Running

## Slide 62: App Lifecycle Management – State Transitions
stop
deactivate
uninstall
install
activate
start
app-hosting install appid myapp package usbflash1:myapp.tar
app-hosting activate appid myapp
app-hosting start appid myapp
app-hosting uninstall appid myapp
app-hosting deactivate appid myapp
app-hosting stop appid myapp
Notes: INSTALL/DEPLOYED: Application is installed on the device. Resources needed by the application is not committed to the application.
ACTIVATED: The resources required by the application is now committed. Associated container artifacts are also generated.
START/RUNNING: Application is now running
STOPPED : Application is stopped.

## Slide 63: List Applications
show app-hosting detail
Switch# sh app-hosting detail appid myapp
State : RUNNING
Author : Cisco Systems, Inc.
Application
Type : Docker
App id : myapp
Version : 3.4
Description : Lubuntu based myapp
Resource reservation
Memory : 1792 MB
Disk : 10 MB
CPU : 6600 units
VCPU : 2
Network interfaces
eth0:
MAC address: 52:54:dd:cd:0f:d4
IPv4 address: 172.26.249.202
show app-hosting list
Switch# sh app-hosting list
App id State
-----------------------------------------------
myapp RUNNING
Sample_app DEPLOYED

## Slide 64: App Resources Configuration
Only cpu, memory, vcpu resource can be changed
Application config vnic and resource changes will only take effect by the next “app-hosting activate” command.
Resource values are application specific and any adjustments need to ensure that the app can run reliably with the new changes.
Switch#conf t Switch(config)# app-hosting appid myapp
Switch(config-app-hosting)# app-resource profile custom
Switch (config-app-resource-profile-custom)# cpu 7400
Switch (config-app-resource-profile-custom)# memory 2048
Switch (config-app-resource-profile-custom)# vcpu 2
Reserved resource specified in app package can be overridden by setting a custom resource profile
app-resource profile custom
Notes: Application config vnic and resource changes will only take effect by the next “app-hosting activate” command.
  (i.e. if the app is already running, stop > deactivate > activate > start is required to use the new resource changes)

## Slide 65: Docker CLIs
IOS CLI | Docker Commands
app-hosting connect appid MYAPP session | docker exec /bin/sh
app-hosting data appid MYAPP copy | docker cp
app-hosting activate appid MYAPP | docker create
app-hosting connect appid MYAPP session CMD | docker exec
app-hosting install appid MYAPP package <MYAPP.tar> | docker load
app-hosting move appid MYAPP log | docker logs
show app-hosting list | docker ps
app-hosting deactivate appid MYAPP | docker rm
app-hosting uninstall appid MYAPP | docker rmi
app-hosting start appid MYAPP | docker start
show app-hosting detail appid MYAPP | docker stats
app-hosting stop appid MYAPP | docker stop

## Slide 66
Demo Time!
App-hosting CLI
IOx Local Manager
IOx Fog Director
DNAC App-hosting

## Slide 67: Summary
Fog computing
App-hosting
  Guestshell
  Docker

## Slide 68: Hands-on
Create a Python script to take desired action
Example : ”no shut” a given interface
csr1000v-4cpu(config)#int lo 100
csr1000v-4cpu(config-if)#shut
csr1000v-4cpu(config-if)#
*Apr 2 07:09:02.978: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback100, changed state to down
*Apr 2 07:09:02.978: %LINK-5-CHANGED: Interface Loopback100, changed state to administratively down
*Apr 2 07:09:05.547: %SYS-5-CONFIG_P: Configured programmatically by process XEP_pnp_python from console as on vty4
*Apr 2 07:09:07.545: %LINEPROTO-5-UPDOWN: Line protocol on Interface Loopback100, changed state to up
*Apr 2 07:09:07.545: %LINK-3-UPDOWN: Interface Loopback100, changed state to up
csr1000v-4cpu(config-if)#

## Slide 69: Continue to study..
Learn network programmability basics (DevNet Video Courses)
  https://developer.cisco.com/video/net-prog-basics/
Python Tutorial
  https://www.learnpython.org/
Docker
  https://docs.docker.com/get-started/